## Slide 1: ECN the identifier of a new service model
Bob Briscoe, BT
Mirja Kuhlewind, David Wagner, Stuttgart Uni
Koen De Schepper, Alcatel-Lucent
IETF-89 TSVAREA Mar 2014
Bob Briscoe & Koen de Schepper are part-funded by the European Community under its Seventh Framework Programme through the Reducing Internet Transport Latency (RITE) project ICT-317700

## Slide 2: outline
classic ECN wasn’t useful enough to deploy
opportunity to identify a new service model using ECN
  consistent low delay service for all
incremental deployment path
take-home message for AQM implementers:
    please allow ECN & loss parameters to be independent

## Slide 3: classic ECN just avoiding loss has not been good enough
classic ECN = “drop equivalence”
    networks & hosts treat ECN & drop identically [RFC3168]
cannot justify the deployment pain*
    ECN largely off-by-default in Internet clients
for a small performance gain
    loss levels are low, and falling
    applications can find other ways to mask losses
ECN can do so much better...
* 2001: arbitrary blocking by firewalls & NATs – largely fixed by 2003
2002-2007: IP/ECN packets triggered 1 bugged home gateway model to crash and 4 to increase drop
2009: some border gateways started zeroing ECN – fixes were rapidly deployed

## Slide 4: Immediate ECN + Smooth TCP response
smoothing congestion signals
inspired by Data Centre TCP (DCTCP)
  AQM: Immediate ECN – remove sluggish signal smoothing
  TCP decrease: proportionate to ECN feedback over an RTT
    deployed extensively in ECN data centres
translate this approach to the public Internet?
  more gain
    promise of consistent low delay for all
  less pain
    removes sensitivity of AQM to sluggish RTT setting
    can start with existing hardware, firmware or software

## Slide 5: consistent low delay for all
line utilisation
buffer occupancy
b u f f e r s i z e
queue management operating point
shallower operating point
good line utilisation
lower queuing delay
buffer kept for bursts
TCP saw-teeth seeking the operating point
smooth TCP: more smaller saw-teeth
Today (at best) TCP on end-systems AQM at bottlenecks
if change bottlenecks alone
change bottlenecks and TCP
cuts delay but poorer line utilisation
time
and highly insensitive to threshold config

## Slide 6: RTT auto-tuning
Drop
new AQMs defer dropping for ~100ms (worst-case RTT)
    no response for 5 CDN RTTs, or 25 media server RTTs
ECN
AQM can signal ECN immediately – no risk of impairment
the transport can smooth out ECN bursts if it chooses
  it knows if it’s RTP or TCP in slow-start or cong-avoidance
then a transport’s smoothing delay is only its own RTT
  short RTT flows can fill troughs and absorb peaks
  no need to make all flows as sluggish as the worst-case RTT
continues progress towards zero config
  line-rate auto-tuning: ARED CoDel  PIE 
  round-trip auto-tuning: Shift smoothing to hosts 
bad queue
good(?) queue
4ms
home media server
20ms CDN
100ms origin
good(?) queue

## Slide 7: deployment problem #I: co-existence of smoothed traffic and existing traffic
data centre TCP was so-called only because it couldn’t co-exist with Internet traffic
for Internet: can’t have a low delay threshold for ECN and a deep threshold for drop in one FIFO queue
drop traffic would push the queue to its own balance point
causing 100% marking of ECN packets
then ECN traffic would starve itself
ECN
drop
Queue
packet mark/drop probability
0
1


## Slide 8: problem #1 co-existence: solution initially use existing network hardware
use weighted RED (WRED) implementation
in an unusual configuration
  one FIFO queue with two instances of RED algo
    smoothed queue for drop (EWMA-constant = 9 say)*
    instantaneous queue for ECN (EWMA-constant = 0)
may require new firmware / software
similar approach possible for ECN in (fq_)CoDel & (fq_)PIE
  please ensure parameters for ECN & drop are independent
* if exponential-weighting-constant = B, then RED smooths the queue over 2B packets if B = 9, RED smooths over 29 = 512 packets if B = 0, RED smooths over 20 = 1 packet (i.e. it doesn’t smooth)
ECN
drop
Inst. queue Smoothed queue
0
1

## Slide 9: problem #1 co-existence: solution results of testing so far
goals: a) robust against starvation; b) rough rate equality
simulated large part of the much larger parameter space
    paper under submission, available on request
curve fit implied an analytical solution would exist
derived relation between ECN & drop curves
  such that n ECN-DCTCP flows and m drop-Reno flows would all have equal rates for any n & m
next steps:
  test theory by simulation
  test whether an approximation to the curve is good enough
Averaged Queue q(wq)
ECN
drop
ECN
drop
Inst. queue Smoothed queue
packet mark/drop probability, p
0
1
ECN
drop
Inst. queue Smoothed queue
0
1
pdrop = 0.4p2ECN
both feasible alternatives
* by Juan Manuel Reyes Espinosa
1
2
3

## Slide 10: deployment problem #2: solution incremental deployment interop between classic and immediate ECN
smoothing congestion signals
smoothed TCP (sndr) requires ‘accurate ECN feedback’ (rcvr)
  tied together by accurate feedback negotiation during 3WHS
server: ECN on-by-default in majority of servers
client: turn ECN on-by-default in client when deploying:
  accurate ECN feedback + ECN fall-back
transport buffers | small smoothed responses to each ECN | one big instant response to ECN per RTT
immediate ECN |  | 1
smoothed ECN | 2 | 
1 more marks from network, but one response per RTT at sender don’t get smoother latency until host upgrades as well (see Tuning ECN for data center networks, Microsoft Research Asia, In Proc CoNEXT’12) 2 doubly smoothed response to congestion
these two ticks are based on conjecture, not experimental evidence (yet)
classic
smoothing congestion signals

## Slide 11: cross-layer / cross-wg impact on IETF
RFC 3168 may not need to be updated (see spare slide)
urgent, given pace of AQM development
wire protocol: the main standards track change
algorithm experimentation expected
 | component | IETF wg | document
3.1 | redefine meaning of ECN CE | tsvwg | Expt update to RFC3168
3.2 | specify ECN behaviour in AQM algos | aqm | CoDel, PIE, ARED
3.3 | specify change to TCP feedback | tcpm | draft-ietf-tcpm-accecn-reqs draft-kuehlewind-accurate-ecn
3.4 | specify change to TCP sender algo | tcpm | draft-bensen-tcpm-dctcp
 | problem | IETF wg formed
1 | real-time media congestion avoidance | rmcat
2 | prevent TCP bloating queues | aqm
3 | prevent TCP’s swings in delay | -

## Slide 12: Immediate ECN concluding messages
promise of consistent low delay for all
    host uses smoother sawteeth
    immediate signals during dynamics not delayed for a worst-case round trip
removes hard-coded round-trip-time from AQMs
can use existing network hardware
AQM implementers note well:
    research in progress
    but please allow ECN & loss parameters to be independent

## Slide 13: Immediate ECN
Q&A
Q1: if subsequent experiments are as promising as these, would there be an appetite in the transport area to tweak the meaning of ECN?
spare slides

## Slide 14: flow separation (FQ_AQM) isolates me from other TCP sawteeth?
it doesn’t isolate me from my own sawteeth
    queue varying between 0-1 RTT unavoidable in access links
    video delivery over TCP needs larger play-out buffer
flow separation
  implies you have to choose the scheduling policy
    IPSec VPNs – FQ gives them 1 flow’s share
    variable rate video wants to vary its share
    LEDBAT wants to take less than its share
  end-to-end principle
    look very hard for an alternative before you break it
?

## Slide 15: which codepoint for immediate ECN?
To use CE for immediate ECN, may not need to update RFC3168 (Addition of ECN to IP):
  ...if the ECT codepoint is set in that packet's IP header ... then instead of dropping the packet, the router MAY instead set the CE codepoint in the IP header.
  An environment where all end nodes were ECN-Capable could allow new criteria to be developed for setting the CE codepoint, and new congestion control mechanisms for end-node reaction to CE packets. However, this is a research issue, and as such is not addressed in this document.
  Could use ECT(1) for immediate ECN
    but this unnecessarily wastes the CE codepoint (who would want ‘sluggish ECN’?)

## Slide 16: a similar coexistence approach should be applicable to other AQMs
ultimately, want to auto-tune against line-rate and RTT
  use a modern AQM that uses queuing delay as its metric
  and separate drop and ECN algos
message for implementers (esp. in silicon)
    ensure parameters can be configured independently for ECN
AQM | smoothing parameter | non-ECN packets | ECN packets
ARED | ewma-const | 9 | 0
PIE | max_burst | 100ms | 0
CoDel | interval | 100ms | 0

## Slide 17: immediate and shallow ECN?
to avoid starvation in any scenario
    if FIFO, min thresholds for ECN & drop need to be the same
    (in theory – to be tested)
first immediate ECN only
    incentivises initial deployment
    performance gain only from immediate ECN
    not from a shallow threshold
    cannot risk lower utilisation for prevalent non-ECN traffic
later, immediate and shallow ECN with shallow drop
    must shift both thresholds together
    as ECN traffic becomes prevalent
      smoother ECN traffic will maintain high utilisation
      also more insensitive to config
ECN
drop
Inst. queue Smoothed queue
0
1


## Slide 18: co-existence results of ‘gating tests’
explored large part of the much larger parameter space
    implemented in Linux 3.2.18; simulated in IKR simlib
    ‘gating tests’: long-running flows only
    paper under submission, available on request
robust against starvation
formula to derive ECN config from drop config to maintain rate fairness
can then find sweet spot for the drop config
Averaged Queue q(wq)
ECN
drop

## Slide 19: a sample of the results so far
early deployment, when traffic mostly drop-based have to set drop (and therefore ECN) threshold deep
as more flows shift to DCTCP, can set both thresholds shallower
Instantaneous queue
Averaged queue (wq)
ECN
drop

## Slide 20: DCTCP in Action
20
Setup: Win 7, Broadcom 1Gbps Switch
Scenario: 2 long-lived flows, K = 30KB
(Kbytes)
Notes: Not ns2.
K = 30KB => 20 packets
20

## Slide 21: Throughput-Latency Tradeoff
18
Parameters: link capacity = 10Gbps RTT = 480μs smoothing constant (at source), g = 0.05.
For TCP:
Throughput → 75%
Throughput > 94% as K  0
Notes: Bandwidth-delay product = 400 x 1500B packets

## Slide 22: DCTCP activity
E2e Transport
  In Windows 8 Server data center template
  I-D for DCTCP feedback (intended EXP) [draft-kuehlewind-tcpm-accurate-ecn-01]
AQM
  Existing kit: Just a degenerate config of RED
  Can be implemented as just a step at K packets (single ‘if’ command)
  For zero-delay can use a virtual queue [RC5670]
    hardware implementations [“How to Build a Virtual Queue from Two Leaky Buckets”]
    see HULL for specifics with DCTCP
Analysis, papers, Linux & ns2 implementation, etc
  <http://www.stanford.edu/~alizade/Site/DCTCP.html>
  SIGCOMM paper gives entry point
Averaged
Figures courtesy of Alizadeh et al

## Slide 23: Data Center TCP Algorithm
Switch side:
Mark packets when Queue Length > K
  Sender side:
  Maintain moving average of fraction of marked packets (α)
  Adaptive congestion window decrease:
B
K
Mark
Don’t
Mark
Notes: very simple marking mechanism
not all the tunings other aqms have
on the source side, the source is tryign to estimate the fraction of packets getting marked
using the obs that there is a stream of ecn marks coming back – more info in the stream than in any single bit
trying to maintain smooth rate variations to operate well even when using shallow buffers, and only a few flows (no stat mux)
F over the last RTT. In TCP there is always a way to get the next RTT from the window size. Comes from the self-clocking of TCP.
Only changing the decrease. Simplest version – makes a lot of sense. So generic could apply it to any algorithm – CTCP, CUBIC – how to cut its window leaving increase part to what it already does. Have to be careful here.
23